## Slide 1: Computer Networks
CSE 4511

## Slide 2: Network
Network: A set of devices (nodes) connected by communication links
Node: Computer, printer, or any device capable of sending and/or receiving data
To be considered effective and efficient, a network must meet a number of criteria

## Slide 3: Type of Connection

## Slide 4: Type of Connection
Point-to-point
  Dedicated link between two devices
  The entire capacity of the channel is reserved
  Ex) Microwave link, TV remote control
Multipoint
  More than two devices share a single link
  Capacity of the channel is either
    Spatially shared: Devices can use the link simultaneously
    Timeshare: Users take turns

## Slide 5: Physical Topology

## Slide 6: Mesh Topology
Dedicated point-to-point link to every other nodes
A mesh network with n nodes has n(n-1)/2 links. A node has n-1 I/O ports (links)
Advantages: No traffic problems, robust, security, easy fault identification & isolation
Disadvantages: Difficult installation/reconfiguration, space, cost

## Slide 7: Star Topology
Dedicated point-to-point link only to a central controller, called a hub
Hub acts as an exchange: No direct traffic between devices
Advantages: Less expensive, robust
Disadvantages: dependency of the whole on one single point, the hub

## Slide 8: Bus Topology
One long cable that links all nodes
tap, drop line, cable end
limit on the # of devices, distance between nodes
Advantages: Easy installation, cheap
Disadvantages: Difficult reconfiguration, no fault isolation, a fault or break in the bus stops all transmission

## Slide 9: Ring Topology
Dedicated point-to-point link only with the two nodes on each sides
One direction, repeater
Advantages: Easy reconfiguration, fault isolation
Disadvantage: Unidirectional traffic, a break in the ring cab disable the entire network

## Slide 10: Hybrid Topology
Example: Main star topology with each branch connecting several stations in a bus topology
To share the advantages from various topologies

## Slide 11: Categories of Networks

## Slide 12: LAN
Usually privately owned
A network for a single office, building, or campus  a few Km
Common LAN topologies: bus, ring, star
An isolated LAN connecting 12 computers to a hub in a closet

## Slide 13: MAN
Designed to extend to an entire city
Cable TV network, a company’s connected LANs
Owned by a private or a public company

## Slide 14: WAN
Long distance transmission, e.g., a country, a continent, the world
Enterprise network: A WAN that is owned and used by one company

## Slide 15: Internetwork
Internetwork (internet) : two or more networks are connected by internetworking devices
Internetworking devices: router, gateway, etc.
The Internet: a specific worldwide network

## Slide 16: Internetwork Example
A heterogeneous network : four WANs and two LANs

## Slide 17: Internet Today
ISP (Internet service providers)
NISP (national ISP)
NAP (network access point)

## Slide 18: Network Models
Layered Tasks
The OSI Model
Layers in the OSI Model
TCP/IP Protocol Suite
Addressing

## Slide 19: Layered Model: Sending a Letter

## Slide 20: OSI Model
ISO is the organization. OSI is the model

## Slide 21: Interaction between layers in the OSI model
Layer and interface

## Slide 22: An exchange using the OSI model
Encapsulation with header and possibly trailer

## Slide 23: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next
Mechanical and electrical specification, the procedures and functions

## Slide 24: Physical Layer: Responsibilities
Physical characteristics of interfaces and media
Representation of bits
Data rate
Synchronization of bits
Line configuration
Physical topology
Transmission mode

## Slide 25: Data Link Layer
The data link layer is responsible for moving frames from one hop (node) to the next
Transform the physical layer to a reliable (error-free) link

## Slide 26: Data Link Layer: Duties
Framing
Physical addressing
Flow control
Error control
Access control

## Slide 27: Hop-to-Hop Delivery

## Slide 28: Network Layer
The network layer is responsible for the delivery of packets from the source host to the destination host

## Slide 29: Network Layer: Duties
Logical addressing and routing

## Slide 30: Transport Layer
The transport layer is responsible for delivery of a message from one process to another

## Slide 31: Transport Layer: Duties
Service-point (port) addressing
Segmentation and reassembly
Connection control
Flow control
Error control

## Slide 32: Reliable Process-to-Process Delivery of a Message

## Slide 33: Session Layer
Session layer is responsible for dialog control and synchronization

## Slide 34: Presentation Layer
Presentation layer is responsible for translation, compression, and encryption

## Slide 35: Application Layer
Application layer is responsible for providing services to the user

## Slide 36: Application Layer: Services
Network virtual terminal
Mail services
File transfer, access, and management
Directory services

## Slide 37: Summary of Layers

## Slide 38: TCP/IP and OSI Model

## Slide 39: TCP/IP Protocol Suite
Host-to-network : Physical and data link layer
  No specific protocol
Network layer
  IP(Internet Protocl), ARP(Address Resolution Protocol), RARP(Reverse ARP), ICMP(Internet Control Message Protocol), IGMP(Internet Group Message Protocol)
Transport layer
  TCP(Transmission Control Protocol), UDP(User Datagram Protocl), SCTP(Stream Control Transmission Protocol),
Application Layer
  Combined session, presentation, and application layers

## Slide 40: Addressing
Four levels of addresses in TCP/IP protocols
Physical (link), logical (IP, network), port, and specific addresses

## Slide 41: Relationship of Layers and Addresses

## Slide 42: Physical Address
A node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.
07:01:02:01:2C:4B A 6-byte (12 hexadecimal digits) physical address.

## Slide 43: Logical (IP) Address
The physical addresses will change from hop to hop, but the logical addresses usually remain the same

## Slide 44: Port Address
The physical addresses change from hop to hop, but the logical and port addresses usually remain the same

## Slide 45: Specific Address
Some application have user-friendly addresses that are designed for that specific address
Example 1: e-mail address: kchung@kw.ac.kr
  Defines the recipient of an e-mail
Example 2: URL (Universal Resource Locator) : www.kbs.co.kr
  Used to find a document on the WWW