## Slide 1: Chapter 22. Network Layer: Delivery, Forwarding, and Routing
21.1 Delivery
21.2 Forwarding
21.3 Unicast Routing Protocols
21.4 Multicast Routing Protocols

## Slide 2: Delivery
The network layer supervises the handling of the packets by the underlying physical networks. We define this handling as the delivery of a packet.
Direct versus Indirect Delivery

## Slide 3: Forwarding
Forwarding means to place the packet in its route to its destination.
Forwarding requires a host or a router to have a routing table
Forwarding techniques to make the size of the routing table manageable
  Next-hop method versus route method
  Network-specific method versus host-specific method
  Default method

## Slide 4: Forwarding Techniques
Route method versus next-hop method

## Slide 5: Forwarding Techniques
Host –specific versus network-specific method
Default method

## Slide 6: Forwarding Process
In classless addressing, we need at least four columns in a routing table

## Slide 7: Example
Make a routing table for router R1, using the configuration in Figure

## Slide 8: Example
Routing table for router R1
Forwarding process for the destination address 180.70.65.140 ?
Forwarding process for the destination address 18.24.32.78 ?

## Slide 9: Address Aggregation
Classless addressing increases the number of routing table entries
To alleviate the problem, the address aggregation is used

## Slide 10: Longest Mask Matching

## Slide 11: Hierarchical Routing
To solve the problem of gigantic routing tables

## Slide 12: Routing Table
Static routing table: created manually
Dynamic routing table: updated periodically by using one of the dynamic routing protocols such as RIP, OSPF, or BGP
Common fields in a routing table
  Flag: U(up), G(gateway), H(host-specific), D(added by redirection), M(modified by redirection)
  Reference count: number of users of this route at the moment
  Use: the number of packets transmitted through this router for the corresponding destination

## Slide 13: Utilities
To find the routing information and the contents of a routing table
netstat and ifconfig

## Slide 14: Routing Protocols
A router consults a routing table when a packet is ready to be forwarded
The routing table specifies the optimum path for the packet: static or dynamic
Internet needs dynamic routing tables to be updated as soon as there is a change
Routing protocols is a combination of rules and procedures for dynamic routing tables
The routing protocols also include procedures for combining information received from other routers
Unicast routing and multicasting routing
RIP (Routing Information Protocol), OSPF (Open Shortest Path First), BGP (Border Gateway Protocol)

## Slide 15: Optimization
Which of the available pathways is the optimum pathway ?
One approach is to assign a cost for passing through a network, called metric
Total metric is equal to the sum of the metrics of networks that comprise the route
Router chooses the route with shortest (smallest) metric
RIP (Routing Information Protocol): hop count
OSPF (Open Shortest Path First): allows administrator to assign a cost based on the type of service required
BGP (Border Gateway Protocol): criterion is the policy

## Slide 16: Intra- and Interdomain Routing
AS (autonomous system): A group of networks and routers under the authority of a single administration
Intradomain routing: inside an AS
Interdomain routing: between ASs
R1, R2, R3, and R4 use a intradomain and an interdomain routing protocol.
The other routes use only intradomain routing protocols

## Slide 17: Popular (Unicast) Routing Protocols

## Slide 18: Distance Vector Routing
The least-cost route between any two nodes is the route with minimum distance
Each node maintains a vector(table) of minimum distances to every node
Distance vector routing table

## Slide 19: Distance Vector Routing: Initialization
At the beginning, each node can know only the distance between itself and its immediate neighbors

## Slide 20: Distance Vector Routing: Sharing
In distance vector routing, each node shares its routing table with its immediate neighbors periodically and when there is a change

## Slide 21: Distance Vector Routing: Updating
When a node receives a two-column table from a neighbor, it need to update its routing table
Updating rule:
  Choose the smaller cost. If the same, keep the old one
  If the next-node entry is the same, the receiving node chooses the new row

## Slide 22: When to Share
Periodic update: A node sends its routing table, normally every 30 s
Triggered update: Anode sends its two-column routing table to its neighbors anytime there is a change in its routing table
Two-node instability

## Slide 23: Two-Node Instability
Defining infinity: To redefine infinity to a smaller number, such as 100
Split horizon: Instead of flooding the table through each interface, each node sends only part of its table through each interface. Node B eliminates the last line of its routing table before it sends it to A
Split horizon and poison reverse: Node B can still advertise the value for X, but if the source of information is A, it can replace the distance with infinity as a warning: “Do not use this value, what I know about this route comes from you.”

## Slide 24: Three-Node Instability
If the instability is between three nodes, stability cannot be guaranteed.

## Slide 25: Routing Information Protocol
RIP: an intradomain routing protocol used inside an AS
Simple protocol based distance vector routing
Metric is simple, a hop count. The distance is defined as the number of links (networks) to reach the destination

## Slide 26: Example of RIP Updating

## Slide 27: Link State Routing
Each node has the entire topology of the domain- the list of nodes and links, how they are connected including type, cost, and condition of the links(up or down)
Node can use Dijkstra’s algorithm to build a routing table

## Slide 28: Link State Knowledge
Each node has partial knowledge: it know the state (type, condition, and cost) of its links. The whole topology can be compiled from the partial knowledge of each node

## Slide 29: Building Routing Table
Creation of the states of the links by each node, called the link state packet (LSP)
Dissemination of LSPs to every other router, called flooding, in an efficient and reliable way
Formation of a shortest path tree for each node
Calculation of a routing table based on the shortest path tree
Creation of LSP
  LSP contains node identity, the list of links (to make the topology), sequence number (to facilitate flooding and distinguish new LSPs from old ones
  LSPs are generated (1) when there is a change in the topology of the domain, (2) on a periodic basis, normally 60 min or 2 h

## Slide 30: Building Routing Table
Flooding of LSPs
  The creating node sends a copy of the LSP out of each interface
  A node compares it with the copy it may already have. If the newly arrived LSP is older than the one it has, it discards the LSP. If it is newer,
  It discards the old LSP and keeps the new one
  It sends a copy of it out of each interface except the one from which the packet arrived
Formation of shortest path tree: Dijkstra Algorithm
  After receiving all LSPs, each node will have a copy of the whole topology. Need to find the shortest path to every other node
  The Dijkstra algorithm creates a shortest path tree from a graph

## Slide 31: Dijkstra Algorithm

## Slide 32: Example of Dijkstra Algorithm

## Slide 33: Routing Table
Each node uses the shortest path tree protocol to construct its routing table
The routing table shows the cost of reaching each node from the root

## Slide 34: Open Shortest Path First (OSPF)
Popular intradomain routing protocol based on link state routing
To handle routing efficiently and in a timely manner, OSPF divides an autonomous system into area
Area is a collection of network, hosts, and routers all contained within an AS
AS can also be divided into many different areas
Area border gateway, backbone router, virtual link

## Slide 35: Metric
The OSPF allows the administrator to assign a cost, called the metric, to each route
The metric can be based on a type of service (minimum delay, maximum throughput, and so on)
Types of Links

## Slide 36: Point-to-Point Link
Transient Link
To connect two routers without any other host or router in between
A network with several routers attached to it

## Slide 37: Stub Link
Stub link is a network that is connected to only one router
Virtual Link
Virtual link created for broken link by administrator

## Slide 38: Graphical Representation of an Internet

## Slide 39: Path Vector Routing
Distance vector routing is subject to instability if there are more than a few hops in the domain of operation
Link state routing needs a huge amount of resources to calculate routing tables. It also create heavy traffic because of flooding
Need for a third routing algorithm for interdomain routing, called path vector routing
Path vector routing is similar to distance vector routing
But, only speaker node creates a routing table and advertises it to speaker nodes in each AS
A speaker node advertises the path, not the metric of nodes

## Slide 40: Path Vector Routing: Initialization

## Slide 41: Path Vector Routing: Sharing and Updating
Sharing: Like distance vector routing, a speaker shares its table with immediate neighbors
Updating: When a speaker receives a two-column table from a neighbor, it updates its own table
  Loop prevention
  Policy routing
  Optimum path

## Slide 42: Border Gateway Protocol (BGP)
Interdomain routing protocol using path vector routing
Types of autonomous systems (ASs)
  Stub AS: only one connection to another AS
  Multihomed AS: more than one connection to other Ass, but still only a source or sink for data traffic
  Transit AS: a multihomed AS that also allows transient traffic
Path attribute
  Well-know attribute
    Well-known mandatory attribute:
      ORIGIN (source of the routing information)
      AS_PATH (the list of ASs)
      NEXT-HOP(the next router)
    Well-known discretionary attribute
  Optional attribute
    Optional transitive attribute
    Optional nontransitive attribute

## Slide 43: BGP Sessions
A session is a connection between BGP routers for the exchange of router information
To create a reliable environment, BGP uses the services of TCP as semipermanent connections
External and internal BGP
  E-BGP sessions: used to exchange information between two speaker nodes belonging to two different ASs
  I-BGP sessions: used to exchange information between two routers inside an AS

## Slide 44: Unicasting
In unicasting, the router forwards the received packet through only one of its interfaces

## Slide 45: Multicasting
In multicast routing, the router may forward the received packet through several of its interfaces.
Broadcasting is a special case of multicasting

## Slide 46: Multicasting vs. Multiple Unicasting
Emulation of multicasting through multiple unicasting is not efficient and may create long delays, particularly with a large group

## Slide 47: Multicasting Applications
Access to distributed databases
Information dissemination
Dissemination of news
Teleconferencing
Distance learning

## Slide 48: Multicast tree
Objectives of multicasting:
  Every member of the group should receive one, and only one, copy of the multicast packet. Nonmember must not receive a copy
  There must be no loops in routing
  The path traveled from source to each destination must be optimal
In a source-based tree approach, the combination of source and group determines the tree (DVMRP, MOSPF, PIM-DM)
In the group-shared tree approach, the group determines the tree (CBT, PIM-SM)

## Slide 49: Multicast Routing
Optimal routing: Shortest path trees
Unicast Routing
  Each router in the domain has a table that defines a shortest path tree to possible destinations

## Slide 50: Shortest Path Tree
Multicast Routing
  Each involved router needs to construct a shortest path tree for each group
Source-Based Tree and Group-Shared Tree
In the source-based tree approach, each router needs to have one shortest path tree for each group

## Slide 51: Shortest Path Tree
In the group-shared tree approach, only the core router, which has a shortest path tree for each group, is involved in multicasting

## Slide 52: Multicast Protocols

## Slide 53: Multicast Link State Routing: MOSPF
Computer Networks
22-53
Multicast link state routing uses the source-based tree approach
n (the number of group) topologies and n shortest path trees made
Each router has a routing table that represents as many shortest path trees as there are groups
MOSPF is an extension of the OSPF protocol that uses multicast link state routing to create source-based trees
MOSPF requires a new link state update packet to associate the unicast address of a host with the group address or addresses the host is sponsoring
MOSPF is a data-driven protocol; the first time an MOSPF router see a datagram with a given source and group address, the router constructs the Dijkstra shortest path tree

## Slide 54: Multicast Distance Vector: DVMRP
Computer Networks
22-54
Multicast distance vector routing uses the source-based trees, but the router never actually makes a routing table
Multicast routing does not allow a router to send its routing table to its neighbors. The idea is to create a table from scratch by using the information from the unicast distance vector tables
Process based on four decision-making strategies. Each strategy is built on its predecessor
  Flooding
  Reverse Path Forwarding (RPF)
  Reverse Path Broadcasting (RPB)
  Reverse Path Multicasting (RPM)

## Slide 55: DVMRP: Strategies
Flooding broadcasts packets, but creates loops in the systems
Reverse path forwarding: RPF eliminates the loop in the flooding process

## Slide 56: DVMRP: Strategies
Computer Networks
22-56
Reverse path broadcasting: RPB creates a shortest path broadcast tree from the source to each destination. It guarantees that each destination receives one and only one copy of the packet
Problem with RPF

## Slide 57: DVMRP: Strategies
Computer Networks
22-57
Reverse path multicasting: RPM adds pruning and grafting to RPB to create a multicast shortest path tree that supports dynamic membership changes

## Slide 58: Core-Based Tree (CBT)
CBT is a group-shared protocol that uses a core as the root of the tree
AS is divided into regions, and core (center router or rendezvous router) is chosen for each region
Each router sends a unicast join message to rendezvous router
When the rendezvous router has received all join messages from every member of the group, the tree is formed

## Slide 59: Sending Multicast Packets
The source sends the multicast packet (encapsulated in a unicast packet) to the core router. The core router decapsulates the packet and forwards it to all interested hosts. Each router that receives the multicast packet, in turn, forwards it to all interested ports

## Slide 60: Protocol Independent Multicast (PIM)
PIM-DM (Dense Mode) and PIM-SM (Sparse Mode)
PIM-DM is used in a dense multicast environment, such as a LAN
PIM-DM is a source-based tree routing protocol that uses RPF and pruning and grafting strategies for multicasting. However, it is independent of the underlying unicast protocol.
PIM-SM is used in a sparse multicast environment such as a WAN
PIM-SM is a group-shared routing protocol that has a rendezvous point as the source of the tree
PIM-SM is similar to CBT but uses a simpler procedure.

## Slide 61: MBONE
To enable multicasting, we make a multicast backbone (MBONE) out of isolated routers, using of the concept of tunneling

## Slide 62: Logical Tunneling
A logical tunnel is established by encapsulating the multicast packet inside a unicast packet
The multicast packet becomes the payload (data) of the unicast packet
So far the only protocol supporting MBONE and tunneling is DVMRP