## Slide 1: PART 5 Transport Layer

## Slide 2: Position of Transport Layer
Responsible for the delivery of a message from one process to another

## Slide 3: Chapter 23. Process-to-Process Delivery UDP, TCP, and SCTP
23.1 Process-to-Process Delivery
23.2 UDP
23.3 TCP
23.4 SCTP

## Slide 4: Types of data deliveries
The transport layer is responsible for process-to-process delivery.
Process (application program ??)

## Slide 5: Client-Server Paradigm
Address required for delivery
Transport layer address: port number
Addressing
Most common process-to-process communication is the client-server paradigm
Operating systems support multiuser and multiprogramming environments.
Local host, local process, remote host, remote process must be defined

## Slide 6: Port Numbers
16 bits between 0 and 65553: ephemeral port number
IANA (Internet Assigned Number Authority) range: well-known ports, registered ports, dynamic ports

## Slide 7: IP Addresses vs. Port Numbers

## Slide 8: Socket address
Process-to-process delivery needs two identifiers, IP address and the port number
Socket address is the combination of an IP address and a port number
A transport-layer protocol needs a pair of socket addresses; the client and server socket address

## Slide 9: Multiplexing and demultiplexing
Addressing mechanism allows multiplexing and demultiplexing by the transport layer

## Slide 10: Connectionless vs. Connection-oriented
Connection-oriented: connection established, data transferred, connection released
  TCP and SCTP
Connectionless: UDP
Reliable vs. Unreliable

## Slide 11: Position of UDP, TCP, and SCTP

## Slide 12: UDP
The User Datagram Protocol (UDP) is called a connectionless, unreliable transport protocol. It does not add anything to the services of IP except to provide process-to-process communication instead of host-to-host communication
UDP is a convenient transport-layer protocol for applications that provide flow and error control. It is also used by multimedia applications.
The calculation of checksum and its inclusion in the user datagram are optional

## Slide 13: Well-known Ports for UDP

## Slide 14: UDP: Checksum
Checksum includes three section: a pseudoheader, the UDP header, and the data from the application layer

## Slide 15: UDP: Checksum
Example for checksum calculation of a simple UDP user datagram

## Slide 16: UDP Operation
Connectionless services
Flow and error control: no control without checksum
Encapsulation and decapsulation
Queuing

## Slide 17: Use of UDP
Suitable for a process that requires simple request-response communication with little concern for flow and error control
Suitable for a process with internal flow and error control mechanisms such as TFTP
Suitable for multicasting
Used for management processes such as SNMP
Used for some route updating protocols such as RIP

## Slide 18: TCP
Transmission Control Protocol
Connection-oriented, reliable transport protocol
It adds connection-oriented and reliability features to the services of IP
Like UDP, TCP uses port numbers as transport-layer addresses
Unlike UDP, TCP is a stream-oriented protocol

## Slide 19: Well-known Ports for TCP

## Slide 20: Sending and Receiving Buffers
Buffering handles the disparity between the speed of the producing and consuming processes
One example: to use a circular array of 1-byte locations

## Slide 21: TCP Segments
IP layer needs to send data in packets not as a stream of byte

## Slide 22: TCP Features
Numbering system: sequence number and acknowledgment number
Byte number: The bytes of data being transferred in each connection are numbered by TCP. The numbering starts with a randomly generated number
The value in the sequence number field of a segment defines the number of the first data byte contained in that segment
The value of the acknowledgment field in a segment defines the number of the next byte a party expects to receive. The acknowledgment number is cumulative

## Slide 23: TCP Segment Format

## Slide 24: TCP Control Field

## Slide 25: A TCP Connection: Establishment
Connection establishment: Three-way handshaking
A SYN segment cannot carry data, but it consumes one sequence number
A SYN + ACK segment cannot carry data, but does consume one sequence number
An ACK segment, if carrying no data, consumes no sequence number
Simultaneous open and SYN flooding attack (denial-of service attack, cookie)

## Slide 26: A TCP Connection: Data Transfer
After connection is established, bidirectional data transfer can take place
Pushing data and urgent data

## Slide 27: A TCP Connection: Connection Termination
Three-way handshaking
The FIN segment consumes one sequence number if it does not carry data
The FIN + ACK segment consumes one sequence number if it does not carry data

## Slide 28: Connection Termination: Half-Close

## Slide 29: Flow Control
A sliding window is used to make transmission more efficient as well as to control the flow of data so that the destination does not become overwhelmed with data. TCP sliding windows are byte-oriented.

## Slide 30: TCP Sliding Window
❏ The size of the window is the lesser of rwnd and cwnd.
❏ The source does not have to send a full window’s worth of data.
❏ The window can be opened or closed by the receiver, but should not be
shrunk.
❏ The destination can send an acknowledgment at any time as long as it
does not result in a shrinking window.
❏ The receiver can temporarily shut down the window; the sender,
however, can always send a segment of 1 byte after the window is shut
down.

## Slide 31: Error Control
Error detection and correction in TCP is achieved through the use of three simple tools: checksum, acknowledgment, and time-out
Checksum: If corrupted, it is discarded and considered as lost
Acknowledgment:
  ACK segments do not consume sequence numbers and are not acknowledged
Retransmission:
  In modern implementations, a retransmission occurs if the retransmission timer expires or three duplicate ACK segments have arrived
  No retransmission timer is set for an ACK segment
  Retransmission after RTO (Retransmission Time-Out): RTO is updated based on the RTT (Round Trip Time)
  Retransmission after three duplicate ACK segments
Out-of-order segments
  Data may arrive out of order and be temporarily stored by the receiving TCP, but TCP guarantees that no out-of-order segment is delivered to the process

## Slide 32: TCP Scenarios
Normal Operation

## Slide 33: TCP Scenarios
Lost Segment
The receiver TCP delivers only ordered data to the process

## Slide 34: TCP Scenarios
Fast retransmission

## Slide 35: SCTP
Stream Control Transmission Protocol (SCTP) is a new reliable, message-oriented transport layer protocol that combines the best features of UDP and TCP
SCTP Services:
  Process-to-process communication: use all well-known ports in TCP
  Multiple streams
  Multihoming
  Full-duplex communication
  Connection-oriented service
  Reliable service

## Slide 36: SCTP Services
Multiple streams: An association in SCTP can involve multiple streams
Multihoming: SCTP association allows multiple IP addresses for each end

## Slide 37: SCTP Features
Transmission sequence number is used to number a data chunk
Stream identifier (SI) to distinguish between different streams
Stream sequence number to distinguish between different data chunks belong to the same stream
Packets: TCP has segments; SCTP has packets
  In SCTP, control information and data information are carried in separate chunks

## Slide 38: Differences between SCTP and TCP
The control information in TCP is part of the header; the control information in SCTP is included in the control chunks
The data in a TCP segment treated as one entity; an SCTP packet can carry several data chunks
The option section, which can be part of a TCP segment, does not exist in an SCTP packet
The mandatory part of the TCP header is 20 bytes, while the general header in SCTP is only 12 bytes
The checksum in TCP is 16 bits; in SCTP, it is 32 bits
The verification tag in SCTP is an association identifier, which does not exist in TCP
TCP includes one sequence number in the header, which defines the number of the first byte in the data section. AN SCTP packet can include several different data chunks
Some segments in TCP that carry control information (such as SYN and FIN) need to consume one sequence number; control chunks in SCTP never use a TSN, SI, or SSN

## Slide 39: Packet, Data Chunks, and Stream
Data chunks are identified by three items: TSN, SI, and SSN. TSN is a cumulative number identifying the association; SI defines the stream; SSN defines the chunk in a stream
Acknowledgment Number
In SCTP, acknowledgment numbers are used to acknowledge only data chunks; control chunks are acknowledged by other control chunks if necessary

## Slide 40: SCTP Packet Format
In an SCTP packet, control chunks come before data chunks
General Header

## Slide 41: SCTP Chunks

## Slide 42: SCTP Association
SCTP, like TCP, is a connection-oriented protocol
A connection in SCTP is called an association to emphasize multihoming
Association establishment requires a four-way handshake
No other chunk is allowed in a packet carrying an INIT or INIT ACK chunk. A COOKIE ECHO or a COOKIE ACK chunk can carry data chunks

## Slide 43: SCTP Association: Data Transfer
Bidirectional data transfer
Like TCP, SCTP supports piggybacking
In SCTP, only DATA chunks consume TSNs; DATA chunks are the only chunks that are acknowledged
The acknowledgment in SCTP defines the cumulative TSN, the TSN of the last data chunk received in order

## Slide 44: Association Termination

## Slide 45: SCTP Flow Control
Flow control in SCTP is similar to that in TCP. But, SCTP use two units of data, the byte and the chunk. The value of rwnd and cwnd are expressed in byte; the value of TSN and acknowledgment are in chunks

## Slide 46: Flow Control Scenario

## Slide 47: SCTP Error Control
SCTP, like TCP, is a reliable transport layer. It uses a SACK chunk to report the state of the receiver buffer to the sender

## Slide 48: Error Control
Sending Data Chunks: Whenever there are data chunks in the sending queue with a TSN greater than or equal curTSN or if there are data chunks in the retransmission queue
(the total size of the data chunks included in the packet must not exceed rwnd - inTransit
Retransmission: Using retransmission timers and receiving four SACKs with the same missing chunks
Generating SACK Chunks: Similar rule used for ACK with the TCP ACK flag
Congestion Control : The same strategies in TCP (Chapter 24). SCTP has slow start (exponential increase), congestion avoidance (additive increase), and congestion detection (multiplicative decrease). SCTP also use fast retransmission and fast recovery